## Slide 1
Transformer Approach
Why Convolutional Transformer: RNNs suffer from vanishing gradients on long sequences (9,212 timesteps). Standard Transformers are O(n²) on sequence length, causing GPU memory overflow. Conv-MHSA (Yang et al. 2022) solves both: 1D convolutions compress the temporal dimension 8x, then self-attention captures temporally distant relationships that CNNs and RNNs cannot detect.
Input time series
Shape: (19540, 9212, 15)
▼
Conv1d (stride=2)
9212 → 4606 timesteps
▼
Conv1d (stride=4)
4606 → ~1152 (8x compression)
▼
Positional encoding
Learnable, adds temporal order
▼
4x Transformer encoder
8 heads, d_model=256, dim_ff=1024
▼
Masked mean pooling
Ignores zero-padded timesteps
▼
Linear(256, 2)
Output: P(at-risk), P(safe)
Key design decisions
Conv compression
Self-attention is O(n²). Without compression, 9212² = 84.9M attention entries causes CUDA OOM. Two Conv1d layers reduce temporal dimension 8x, cutting attention memory by 64x.
Temporal augmentations
Cutout, cutmix, and mixup (40% probability each) applied during training only. Without augmentations, the model overfits severely and collapses to majority-class prediction, consistent with the Conv-MHSA paper findings.
PR-AUC checkpoint
Model saved based on validation PR-AUC instead of recall or F1. This prevents the degenerate predictor trap where predicting all flights as one class achieves high recall but is useless.
LR = 3e-5 + CosineAnnealingLR
Learning rate matched to the Conv-MHSA paper. Manual experiments showed 33x difference between collapsed model (LR=1e-3) and optimal (LR=3e-5). Cosine schedule smoothly decays LR each epoch.
Masked mean pooling
Variable-length flights are zero-padded to 9,212 timesteps. Masked pooling averages only real timesteps, preventing padding from diluting the signal for short flights.
Hyperparameter tuning
Exp | Flights | D_MODEL | LR | PR-AUC | Finding
1 | 500 | 64 | 1e-3 | 0.512 | LR too high, collapsed
2 | 500 | 128 | 3e-5 | 0.573 | Collapse broken, slow
3 | 500 | 128 | 1e-4 | 0.666 | Sweet spot for subset
4 | 500 | 256 | 1e-4 | 0.731 | More capacity helped
5 | 19,540 | 256 | 3e-5 | 0.816 | Full dataset, best
Optuna validation: 20 trials on 500 flights + 12 trials on 2,000 flights confirmed that manual Experiment 4 parameters were already optimal. Optuna could not beat the manually tuned configuration.
Final configuration
D_MODEL = 256 N_HEAD = 8
NUM_LAYERS = 4 DIM_FF = 1024
LR = 3e-5 DROPOUT = 0.1
BATCH_SIZE = 2 EPOCHS = 20
Optimizer: AdamW
Scheduler: CosineAnnealingLR
Checkpoint: best val PR-AUC
Augmentations: cutout + cutmix + mixup
*Hyperparameters tuned via manual experiments (Exp 1-4) on 500-flight subset, then validated with Optuna (20 + 12 trials)

## Slide 2
Transformer Approach
Why Convolutional Transformer: RNNs suffer from vanishing gradients on long sequences (9,212 timesteps). Standard Transformers are O(n²) on sequence length, causing GPU memory overflow. Conv-MHSA (Yang et al. 2022) solves both: 1D convolutions compress the temporal dimension 8x, then self-attention captures temporally distant relationships that CNNs and RNNs cannot detect.
Architecture
Input time series
Shape: (19540, 9212, 15)
▼
Conv1d (stride=2)
9212 → 4606 timesteps
▼
Conv1d (stride=4)
4606 → ~1152 (8x compression)
▼
Positional encoding
Learnable, adds temporal order
▼
4x Transformer encoder
8 heads, d_model=256, dim_ff=1024
▼
Masked mean pooling
Ignores zero-padded timesteps
▼
Linear(256, 2)
Output: P(at-risk), P(safe)
Key design decisions
Conv compression
Self-attention is O(n²). Without compression, 9212² = 84.9M attention entries causes CUDA out-of-memory. Two Conv1d layers with stride 2 and stride 4 reduce the temporal dimension 8x (9,212 → ~1,152 timesteps), cutting attention memory by 64x. Each layer uses BatchNorm + GELU activation + Dropout.
Temporal augmentations (training only)
Three augmentations applied in the DataLoader with 40% probability each: Temporal Cutout (zeros out a random time segment on random channels), Temporal Cutmix (replaces a segment with data from another flight), and Temporal Mixup (blends channels with another flight). Without these augmentations, the model overfits and collapses to majority-class prediction, consistent with the Conv-MHSA paper.
PR-AUC checkpoint and hyperparameter tuning
Model checkpoint saved based on validation PR-AUC instead of recall or F1. This prevents the degenerate predictor trap where predicting all flights as one class achieves high recall but is useless. Manual experiments (5 configurations on 500-flight subset) found the optimal hyperparameters, then Optuna validated the search on 500 and 2,000 flights using warm-start seeding (injecting best manual config as Trial 0), locked proven parameters (D_MODEL=256, DIM_FF=1024), and HyperbandPruner for early stopping of underperforming trials. Optuna confirmed the manually tuned configuration was already optimal. Final model trained on full 19,540 flights.
Masked mean pooling
Variable-length flights (100 to 9,212 timesteps) are zero-padded to uniform length. Masked mean pooling averages only over real timesteps, ignoring padding. Without masking, short flights would be diluted by thousands of zero-valued timesteps, degrading prediction accuracy.
Final config: D_MODEL=256 | N_HEAD=8 | NUM_LAYERS=4 | DIM_FF=1024 | LR=3e-5 | DROPOUT=0.1 | BATCH=2 | EPOCHS=20 | AdamW + CosineAnnealingLR | Augmentations: cutout + cutmix + mixup
*Hyperparameters tuned via manual experiments (5 configs) on 500-flight subset, validated with Optuna (20 trials on 500 flights + 12 trials on 2,000 flights), then trained on full 19,540 flights

## Slide 3
Transformer Results
Model evaluation
Split | Accuracy | Precision | Recall | F1 | ROC-AUC | PR-AUC
Val | 0.7015 | 0.6421 | 0.5799 | 0.6843 | 0.7590 | 0.8210
Test | 0.6970 | 0.6280 | 0.5990 | 0.6790 | 0.7538 | 0.8163
Why these results matter
Small gap between val and test performance (PR-AUC 0.821 vs 0.816) indicates the model generalizes well with minimal overfitting. PR-AUC of 0.816 exceeds the original Conv-MHSA paper benchmark on the NGAFID-MC dataset.
Threshold sweep analysis
Operating point | Threshold | Precision | Recall | F1 | Accuracy | False alarms / 100 | Missed risks / 100
Best F1 | 0.17 | 0.63 | 0.63 | 0.69 | 0.70 | 37 | 37
Recall ~75% | 0.03 | 0.58 | 0.76 | 0.68 | 0.68 | 42 | 24
Recall ~90% | 0.02 | 0.53 | 0.89 | 0.63 | 0.63 | 47 | 11
Confusion matrix (test)
Predicted
Risk
Safe
Risk
Safe
Actual
710
474
421
1326
ROC curve (test)
Chart: 
| 0 | 0.01 | 0.03 | 0.05 | 0.08 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6 | 0.65 | 0.7 | 0.8 | 0.9 | 1
ROC (AUC=0.754) | 0 | 0.05 | 0.15 | 0.25 | 0.35 | 0.4 | 0.48 | 0.55 | 0.6 | 0.65 | 0.69 | 0.73 | 0.76 | 0.79 | 0.82 | 0.85 | 0.88 | 0.9 | 0.94 | 0.97 | 1
FPR_diag | 0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1
Random | 0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1
Key insights
PR-AUC 0.816 exceeds the original Conv-MHSA paper benchmark on the NGAFID-MC dataset, validating the architecture for a larger dataset (19,540 vs 7,505 flights).
On the test set, model correctly identifies 710 at-risk flights but misses 474, while producing 421 false alarms.
Moving from Best-F1 to Recall-90% cuts missed risks from 37 to 11 per 100 flights, trading off more false alarms (37 to 47).
ROC-AUC 0.754 tops MiniRocket (0.740) and XGBoost baseline (0.69), demonstrating the Transformer's superior ranking ability.
The 5-day prediction horizon (rul_5d) offers the best operational trade-off: F1=0.739, catching 77% of at-risk flights.
*Threshold tuning was performed on validation data. Test set results reported above.

## Slide 4
Transformer Results
Model evaluation (rul_2d)
Split | Accuracy | Precision | Recall | F1 | ROC-AUC | PR-AUC
Val | 0.7015 | 0.6421 | 0.5799 | 0.6843 | 0.7590 | 0.8210
Test | 0.6970 | 0.6280 | 0.5990 | 0.6790 | 0.7538 | 0.8163
Why these results matter
Small gap between val and test (PR-AUC 0.821 vs 0.816) indicates the model generalizes well. PR-AUC 0.816 exceeds the Conv-MHSA paper benchmark on NGAFID-MC.
Threshold sweep analysis
Operating point | Threshold | Precision | Recall | F1 | Accuracy | False alarms / 100 | Missed risks / 100
Best F1 | 0.17 | 0.63 | 0.63 | 0.69 | 0.70 | 37 | 37
Recall ~75% | 0.03 | 0.58 | 0.76 | 0.68 | 0.68 | 42 | 24
Recall ~90% | 0.02 | 0.53 | 0.89 | 0.63 | 0.63 | 47 | 11
Confusion matrix (test)
Predicted
Risk
Safe
Risk
Safe
Actual
710
474
421
1326
ROC curve (AUC = 0.7538)
Chart: 
| 0 | 0.01 | 0.03 | 0.05 | 0.08 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6 | 0.65 | 0.7 | 0.8 | 0.9 | 1
ROC (AUC=0.754) | 0 | 0.05 | 0.15 | 0.25 | 0.35 | 0.4 | 0.48 | 0.55 | 0.6 | 0.65 | 0.69 | 0.73 | 0.76 | 0.79 | 0.82 | 0.85 | 0.88 | 0.9 | 0.94 | 0.97 | 1
FPR_diag | 0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1
Random baseline | 0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1
Key insights
PR-AUC 0.816 exceeds the original Conv-MHSA paper benchmark on NGAFID-MC, validating the architecture for a larger dataset (19,540 vs 7,505 flights).
On the test set, model correctly identifies 710 at-risk flights but misses 474, while producing 421 false alarms.
Moving from Best-F1 to Recall-90% cuts missed risks from 37 to 11 per 100 flights, trading off more false alarms (37 to 47).
ROC-AUC 0.754 tops MiniRocket (0.740) and XGBoost baseline (0.69), demonstrating the Transformer's superior ranking ability.
The 5-day horizon (rul_5d) offers the best operational trade-off: F1=0.739, catching 77% of at-risk flights.
*Threshold tuning was performed on validation data. Test set results reported above.